## Slide 1: Electricity and Magnetism
Transformers and RMS Vaues

## Slide 2: Electromagnetic Induction
Recall: Faraday’s Law of Electromagnetic Induction
When there is a change in the magnetic flux passing through a coil, a voltage is induced in the coil. The strength of the voltage is proportional to the rate of change of flux passing through the coil
…and Lenz’s Law of Electromagnetic Induction
The direction of the induced current is such as to oppose the change causing it

## Slide 3: Electricity Generation
To generate electricity, we need a constantly changing magnetic field passing through a coil
See phet demo here…
To keep the magnet (or the coil) turning, we can use…..
wind
water
fossil fuels + steam etc…

## Slide 4: Electricity Generation: rms values
The constantly changing magnetic field creates a constantly changing voltage….
….and a constantly changing current
V/V
t/s
I/A
t/s

## Slide 5: Electricity Generation: rms values
Compare two circuits, one a.c. and the other d.c.
In both cases the resistor will heat up
What d.c. voltage would have the same heating effect as 10 V?
What is the rms value of 10 V?
same question

## Slide 6: Electricity Generation: rms values
Sample Question: What is the rms value of an alternating voltage with a peak value if 324 V
In Ireland, mains voltage is 230 V - but this is the rms value. Peak value of V = 324 V

## Slide 7: Transformers
Transformers are all around us…..
…. ‘Chargers’ use transformers to change voltage for our phones
230 V a.c. in
5 V d.c. out

## Slide 8: Transformers
An alternating voltage connected to the input…
…creates a constantly changing magnetic field…..
…creates an alternating voltage at the output
primary coil secondary coil
Np/s = no. of turn in the primary/secondary coils

## Slide 9: transformers
Sample Question:
In a transformer, the primary coil has 150 turns and the secondary has 50 turns. If the input voltage is 13 V, what would you expect the output voltage to be?
Is this a step-up or a step-down transformer?