## Slide 1: 2.1 Heat and Temperature
Cosmic Background Radiation: 2.7 K
CC0
Notes: CBR is key evidence for the current Big Bang theory
A black body in intergalactic space will cool to this temperature of 2.7 K and remain at this temperature. If the body was colder, it would heat up to 2.7 K.

## Slide 2: Physics specification 2.1
Students should be able to
1. analyse the suitability of materials for use as thermometers using primary and secondary data
Students learn about
A definition of temperature
thermometric properties of materials
thermometer as a device
the Kelvin and Celsius temperature scales
2.1. The transfer of heat energy and temperature change
Temperature and Thermometers

## Slide 3: Physics specification 2.1
Students learn about
relationships between heat energy and temperature change
  heat capacity:
  Specific heat capacity:
  Latent heat:
  Specific latent heat:
2.1. The transfer of heat energy and temperature change
Heat Models

## Slide 4: Physics specification 2.1
Students should be able to
2. determine specific heat capacity using primary data (solid or liquid) and secondary data (solid and liquid)
3. determine the specific latent heat using primary data (vaporisation of steam or fusion of ice) and secondary data (vaporisation of steam and fusion of ice)
4. verify mathematical models of heat energy, latent heat and temperature change using secondary data
5. solve real life problems involving heat transfer, change of state and improving efficiency
Heat Models
2.1. The transfer of heat energy and temperature change

## Slide 5: Physics specification 2.1
Students learn about
the concept of a heat pump
particle models of heating; conduction, convection, changes of state
the concept of efficiency
U-value as the rate of transfer of heat through a material
2.1. The transfer of heat energy and temperature change
Heat transfer and Efficiency

## Slide 6: Physics specification 2.1
Students should be able to
5. solve real life problems involving heat transfer, change of state and improving efficiency
6. investigate the impact of insulation on energy consumption and sustainability using secondary sources
2.1. The transfer of heat energy and temperature change
Heat transfer and Efficiency

## Slide 7: Physics specification 2.1
Removed from course: gas thermometers? and graduation
Added to course: suitability of materials for use as thermometers, Particle models, experiments to verify as opposed to determine

## Slide 8: Revision summary
Key definitions: Heat, Temperature, Absolute zero, kelvin, Thermometric properties, Thermocouple, Thermistor, Heat Capacity, Specific Heat Capacity, Latent Heat, Specific Latent Heat, Efficiency, U-value, conduction, convection, radiation.
Solve problems using , θ (℃) = T (K) - 273.15
Describe and explain heat pump, melting, evaporating, solid, liquid, gas, conduction, convection, radiation using particle model and mathematical models where appropriate.
Experimental: Compare thermometer materials (primary and secondary data). Determine and using primary and secondary data. Verify heat models with secondary data.
Investigate insulation vs energy consumption using secondary sources.

## Slide 9: What is meant by Temperature?
Temperature is a measure of hotness or coldness. 2016

## Slide 10: Describe the particle model of heat.
Particle = atom or molecule.
Heat gives energy to the particles.
Temperature is due to the kinetic energy of the particles.
Changes in potential energy (e.g. during melting) do not contribute to temperature.
Vibrating molecule
In solids, the particles vibrate, in liquids and gases they move and collide.

## Slide 11: Can you have a temperature below 0 ℃
Yes, a freezer w
Liquid nitrogen boils at
Liquid Helium boils at
CC0
CC0
CC0
0℃
-100℃
-200℃

## Slide 12: Is there a “lowest temperature”?
Yes
The lowest temperature possible is −273.15 ℃
is called absolute zero
If we could reach absolute zero, atoms would stop vibrating
0℃
-100℃
-200℃
-273℃

## Slide 13: What temperature scale starts at absolute zero?
The kelvin scale
0℃
-100℃
-200℃
-273℃
0 K

## Slide 14: What is the SI Unit of temperature?
The kelvin (K)
Vector or Scalar?
Scalar

## Slide 15: What is the kelvin scale based on?
Absolute zero = 0 K.
The same unit increase as Celsius. ( is same)
274.15 K = 1℃
273.15 K = 0℃
0 K = -273.15℃
= 1 K = 1℃

## Slide 16: What is the relationship between Celsius and Kelvin?
θ (℃) = T (K) - 273.15
Formula book p 58

## Slide 17: Example 1: Temperature conversion
Convert 100 K to degrees Celsius
Formula book p 58
K
o​C
0
-273.15
273.15
0
100 K
Must be about –170℃
a drawing helps avoid mistakes:
θ (℃) = T (K) - 273.15

## Slide 18: Example 2: Temperature conversion
Convert 56℃ to kelvin
Formula book p 58
K
o​C
0
-273.15
273.15
0
56℃
Must be more than 273 K
drawing:
θ (℃) = T (K) - 273.15
⇒T (K) = θ (℃) + 273.15

## Slide 19: Exercise Temperature conversions
Convert 700℃ to kelvin
Convert 700 K to ℃
700℃ = 973.15 K
700 K = 426.85℃

## Slide 20: What is the difference between heat and temperature?
Heat is a form of energy. HL 2016
Temperature is a measure of hotness. HL 2016

## Slide 21: Thermometers

## Slide 22: How do you measure temperature?
Liquid expands into the capillary tube
We measure temperature indirectly through its effects.
For example, the expansion or contraction of a liquid.

## Slide 23: What is a Thermometric Property?
A property that changes measurably with temperature. HL 2015
Example:
length of liquid

## Slide 24: What is the thermometric property of a liquid-in-glass thermometer?
A liquid-in-glass thermometer has a very thin tube into which the liquid can expand. This is called a capillary tube.
Thermometric property = length of the column of liquid.
Length of a column of liquid.

## Slide 25: What is a Resistance Thermometer?
A thermometer whose sensor is made from thin metal.
The most common metals are
Platinum
Copper
Nickel
Platinum resistance thermometers
Top: wire wound
Lower: Thin film
CC0

## Slide 26: Miniature Resistance devices
Thin film (nanometres) of platinum, nickel or copper
Example:
a Pt100 device has a resistance of 100 Ω at 0℃ and 135 Ω at 100℃
2 mm

## Slide 27: What is the thermometric property of a Resistance Thermometer?
The resistance of a metal increases approximately linearly with temperature.
thermometric property = Resistance
Heat
Ohmmeter
Thin metal wire or film
Platinum has the biggest temperature range and is the most stable over time. It is also the most expensive.

## Slide 28: What is a Thermistor?
a semiconductor with 2 connecting wires.
resistance (ohms) changes with temperature.
used in electronic thermometers and thermostats.

## Slide 29: What is the thermometric property of a Thermistor?
Resistance can be measured with an ohm-meter.
Resistance of a thermistor usually decreases with temperature.
Heat
Ohmmeter
thermometric property = resistance
Thermistor

## Slide 30: What is a Thermocouple?
V
Two different metals joined together in a circuit. If there is a difference in temperature in the circuit, a small voltage will be generated
Copper wire
Steel wire
The size of the voltage varies with the temperature difference.
Voltmeter
Hot
Cold

## Slide 31: What is the thermometric property of a Thermocouple?
V
R Downey
Voltage can be measured with a voltmeter set to milli-volts
thermometric property = voltage (emf)
Heat
Ice
Copper wire
Steel wire
Water

## Slide 32: What is the thermometric property of this gas thermometer.
Mass is fixed (air cannot escape).
Pressure is constant (Atmospheric pressure).
If the temperature changes the volume changes and liquid moves.
thermometric property = volume of the gas at constant pressure
Coloured liquid
Test tube with air
R Downey

## Slide 33: Analyse the suitability of materials for use as thermometers
Key features of a thermometer:
Repeatability, stability and accuracy
Sensitivity (e.g. ohms per ℃)
Response time
Heat capacity
Temperature range
Size

## Slide 34: Thermocouples vs platinum resistance thermometer in the Space Shuttle
The space shuttle was the first spacecraft to use a re-usable rocket engine.
In the original design, platinum resistance thermometers monitored engine temperature.
After several flights, the thermometers began to fail. They were subject to too many cycles between extremely low and extremely high temperatures.
They were replaced by thermocouples, not for accuracy but for robustness.
CC0

## Slide 35: Plot Resistance vs Temperature for a copper wire.
Standard Thermometer
Set the multimeter to 200Ω setting
Gradually heat the water.
Note the temperature and the resistance at different points
Plot a R vs T
Water
Ohm-meter
Long Thin Copper wire
Heat
Experiment notes below
Ω 200
2000
Notes: If you have a pre-constructed metal resistance thermometer, then use it to save trouble.
Alternatively use for example 10 meters of laminated copper wire with a diameter of about 0.13 mm (quite thin). This will give about 10 ohms resistance. Wind the wire about something insulating and non soluble (e.g. test tube or pvc pipe). Use insulating tape to hold it in place. The lamination will ensure that the wire does not short circuit and reduce the effective length however a neat coil is recommended as a further precaution against shorting.
Be sure the scrape the lamination off both ends of the wire for attaching to the ohmmeter. Most ohm-meters have a resolution of 0.1 ohm, hence the need get a resistance of about 10 ohms of wire. This needs to be prepared and tested before class as it is fiddley and time consuming. Try to make something you can re-use.
Nichrome wire is problematic as its resistance does not change that much with temperature.
Some recommend glycerol instead of water because of the lower electrical conductivity of glycerol, however the difference is negligible and unlikely to alter any readings in a school lab. Water is shown in a partially drawn diagram in the Ordinary Level Sample paper 1 issued for the new specification.

## Slide 36: Plot Resistance vs Temperature for metal
Resistance
Temperature (℃)
resistance increases with temperature.
very linear within the measurement range – particularly for platinum.
Bureau International des Poids et Mesures use Platinum resistance thermometers to make standard thermometers.

## Slide 37: Plot the Resistance Temperature curve of a thermistor
Standard Thermometer
Set the multimeter to 20kΩ setting.
Gradually heat the water.
Note the temperature and the resistance at different points
Plot R vs T
Water
Ohm-meter
Thermistor
Heat
Notes: Some people recommend glycerol instead of water because of the lower electrical conductivity of glycerol, however the difference it makes is tiny. Some say it makes better thermal contact however, international calibration protocols recommend a liquid bath of water, oil or salt and do not mention glycerol. Water is shown in a partially drawn diagram in the Ordinary Level Sample paper 1 issued for the new specification.

## Slide 38: Temperature vs Resistance – Thermistor
Resistance
Temperature (℃)
resistance decreases with temperature (mostly).
non-linear.
Very sensitive
A microprocessor can calculate the correct temperature.

## Slide 39: Compare resistance temperature curves for two metals
Standard Thermometer
Water
Ohm-meters
RTDs
Heat
Measure resistance and temperature for platinum and nickel RTDs and plot the resistance temperature curves
OR use copper and nichrome wires instead of RTDs
Notes: RTDs are low-cost temperature sensors and can be purchased as a component. Platinum is the most common type but Nickle versions are sometimes available. Nickle has greater heat sensitivity which should give a nice comparison.

## Slide 40: Recap
Accuracy: Closeness to true value
Resolution: The smallest detectable change
Precision: repeatability
Ice bath with stirring rod
0.5℃
Accuracy: 0.5℃ error
Resolution: 0.1℃
Precision: If it reads 0.5℃ every time we measure, then we have good precision.
Example
Notes: A stirred ice bath with plenty of crushed ice in water is a simple and accurate temperature reference for checking thermometers. Boiling point is much more problematic. Apart from scalding risks, variations in air pressure and temperature variations within the boiling liquid make it unreliable.

## Slide 41: Example 3
Compare these resistance-temperature curves. State which material you would choose for measuring body temperature and justify your choice.
Resistance
Temperature (℃)
thin copper wire
thin nichrome wire
Manganese oxide thermistor
Answer A: the thermistor because of smaller size and greater sensitivity to temperature change
Answer B: copper because of linear relationship and adequate sensitivity
37℃

## Slide 42: Exercise
Which thermocouple would work best for temperatures below 100℃ when used with a multimeter with 0.1 mV resolution? Justify your answer.
CC0
Type C, D or Pt Mo 5-0.1 are best because they have the steepest curves below 100℃. The slope is approximately 10 mV over 500℃ so the meter will be able to detect a temperature change every 5℃. However, this is not particularly good and another means of measuring the voltage is desirable.
PtMo are specially suited for nuclear reactors as they are less affected by radiation

## Slide 43: Exercise
Which thermocouple would you choose for work at temperatures ranging from 1 K to 20 K. Justify.
CC0
Conversion: 20 K = -253℃
Chromel-AuFe0.07 is most linear and has the greatest slope making it the most sensitive in the range.

## Slide 44: Exercise
For a given temperature, a thermistor’s resistance can drift over time due to aging effects (e.g. chemical changes in the material).
A thermistor-based thermometer which used to consistently read 0.0℃ in an ice bath now reads -0.4℃ every time it is immersed in an ice bath.
What has changed – its accuracy or its precision or both?
The accuracy has reduced, the precision has not changed

## Slide 45: Exercise
A platinum and a nickel resistance thermometer are compared on the graph below. Both have the same resistance at 0℃. Platinum is generally chosen because of its stability over time. Suggest a reason based on the graph why a manufacturer might base a thermometer design on nickel.
The nickel thermometer has greater sensitivity, ie its resistance changes by a greater amount for a given change in temperature, this makes it easier to detect small temperature changes.
Resistance
Temperature (℃)
Platinum
Nickel

## Slide 46: Heat
CC0

## Slide 47: What is Heat?
Heat is a form of Energy. HL 2016

## Slide 48: What is Heat Capacity?
The energy needed to change the temperature of a body by 1 K.
What is the Symbol?
C (big C)
HL 2022

## Slide 49: How long does it take to boil a kettle?
Full kettle – about 6 minutes
Half full kettle – about 3 minutes
The full kettle needs more energy to raise the temperature by the same amount.
We say the full kettle has more Heat Capacity

## Slide 50: What is the SI Unit of Heat Capacity?
The joule per kelvin (J K⁻¹​​).

## Slide 51: Write the equation for Heat Capacity. (big C)
U
Big C applies to an object rather than a substance this piece of copper rather than copper
Q = Heat to change temperature
C = Heat capacity
= Change in Temperature

## Slide 52: Temperature units in heat problems
Most of the numerical questions quote temperature in Celsius.
Do we need to convert to kelvin?
Not when the problem involves a change in temperature
is the same in °C as in K

## Slide 53: Example 4
Temperature rise is 73°C
Temperature rise = 73 K.
Q =73×500 = 36500 J
Every object has a heat capacity. A piece of metal with a heat capacity of 500 J K⁻¹ is heated from -3°C to +70°C. How much heat was used?
C = heat capacity

## Slide 54: Example 5
New Temperature = 70°C.
A piece of metal at 20°C with a heat capacity of 400 J K⁻¹ is heated with 20 000 J. What temperature will it reach?
C = heat capacity
°C

## Slide 55: Exercise with
An object has a heat capacity of 500
If the object is brought from 30℃ to 40℃, how much energy is used.
If the object is at 20℃ and is heated with 1000 J of energy, what will its new temperature be?
5000 J
22℃

## Slide 56: What is Specific Heat Capacity?
The energy to change the temperature of one kilogram of a substance by one kelvin.
What is the Symbol?
c (small c)
HL 2018, 2021, 2022

## Slide 57: Cooking oil vs water
It takes almost twice as much energy to heat a kg of water to the same temperature as it does a kg of cooking oil.
Water has a higher Specific heat capacity.
Specific heat capacity is a property of a substance.
Oil
Water
1kg
1kg

## Slide 58: What is the SI Unit of Specific Heat Capacity?
The joule per kilogram per kelvin
(J kg⁻¹ K⁻¹).

## Slide 59: Write the equation for Specific Heat Capacity. (small c)
Q = Heat energy added / lost
m = Mass
c = Specific Heat Capacity
= change in Temperature
Provided No Change of State

## Slide 60: Example 6
Temperature difference is 18+50 = 68°C = 68 K.
Q = mcΔθ = 0.5×385×68 = 13 090 J
Specific heat capacity refers to a substance rather than an object. 500 g of copper is heated from -18°C to 50°C. Calculate the heat used.
The specific heat capacity of copper is 385 J kg⁻¹ K⁻¹.
This problem involves “little c” i.e. specific heat capacity

## Slide 61: Exercise with
Copper has a specific heat capacity of 385 J kg⁻¹ K⁻¹
(i) If 2 kg of copper is brought from 30℃ to 40℃, how much energy is used?
(ii) If 500 grams of copper is at 20℃ and is heated with 1000 J of energy, what will its new temperature be?
7700
25.2℃

## Slide 62: Example 7
= 87.78 s
= 175,560 J
Specific Heat Capacity of Water =
A 2 kW electric kettle raises the temperature of 1 kg of water from 18°C to 60°C. How long will it take assuming no heat loss?

## Slide 63: Exercise
What is the minimum time it will take to bring 8 kg of water from 18°C to 100°C in an electric boiler rated at 2 kW?
= 1371 s
= 2742 kJ
Specific Heat Capacity of Water =
= 22.9 mins

## Slide 64: Example 8
c = 907 J per kg per K
The correct answer for aluminium is 897 J kg⁻¹ K⁻¹, calculate the percentage error.
= 1.1%
To determine the specific heat capacity of a substance, we measure how much energy it takes to raise the temperature of a known mass.
32665 J of energy were used to heat 1.2 kg of aluminium from 5°C to 35°C. Calculate the specific heat of the aluminium.

## Slide 65: Exercise
Calculate the specific heat capacity of cooking oil if it took 2 mins 20 seconds to heat 50 g from 17°C to 22°C using an electric heater which output a constant 4 W of heat. Ignore any heat lost.
2240 J kg⁻¹ K⁻¹

## Slide 66: More complex calculations
Heat calculations frequently involve:
Heating two items together to the same temperature
Heat transfer between two objects starting at different temperatures

## Slide 67: Heating two items together
Example: heating 1.2 kg or water in a 0.5 kg aluminium container to raise the temperature by 7°C
You heat the water and the aluminium to the same temperature
m is different, c is different is the same

## Slide 68: Heat transfer
Example: 1.2 kg water at 100°C added to a 0.5 kg aluminium container at 20°C
Result:
Container heats up
Water cools down
An equilibrium temperature is reached
Water
Aluminium
20°C
100°C
equilibrium temperature
100°C
20°C

## Slide 69: Calculate final temperature
Water
Aluminium
=
Heat lost
Heat gained
=
are different for water and the aluminium
=
Trick: Let = final temperature,
=
Water
aluminium
20°C
100°C
=
100°C
20°C

## Slide 70: Complete the calculation
=

## Slide 71: About subscripts
=
m is the symbol for mass. To avoid confusion, we use a small letter after each m to distinguish if it refers to water or to aluminium.
This is called a subscript.
Subscripts to indicate water
subscripts to indicate aluminium

## Slide 72: Example 9 (heating together)
Q=0.06(4184)(9)+0.035(385)(9)
Q=2259.4 + 121.3 = 2381 J
= 4184
= 385
If water is heated in a metal container, the container will also be heated. 60 g of water in a 35 g copper container is brought from 15°C to 24°C. Calculate the heat energy supplied.

## Slide 73: Example 10 (heat transfer)
Heat gained by water = heat lost by copper
70 g of water at is heated by adding 50 g of copper pellets which were heated to 75℃. Calculate the final temperature of the mixture assuming no heat loss.
Note, two

## Slide 74: Exercise
Heat gained by water = heat lost by metal
20 ball bearings with a heat capacity of 75 J K⁻¹ each at a temperature of 90℃ are immersed in 200 g of water which is initially at a temperature of 15℃ in an insulated container. Ignoring the heat capacity of the container, what temperature will the water rise to.
Specific heat capacity of water = 4180 J kg⁻¹ K⁻¹

## Slide 75: Exercise
Let = final temperature
Heat Lost = Heat gained
0.05(390)()=0.12(4180)(-16)
1755-1 = 5-8025.6
1755+8025.6 = 51
9780.6 = 5
50g of copper pellets at 90°C is added to 120 g of water at 16°C in an insulated container. Find the final temperature of the mixture.
Specific Heat Capacity: Water =
Copper =

## Slide 76: Exercise
A teapot is made of 520 g of steal. The teapot is at 20°C before 0.8 litres of water at 100°C are poured in. The teapot and water come to an equilibrium temperature a few seconds later. Calculate this temperature assuming no heat loss to the surrounds.
Specific Heat Capacity: Water =
Steel =
Density of water = 1 gramme per cubic cm
°C

## Slide 77: Example 11 (experiment)
= 385
60 g of water was heated in a 35 g copper container and brought from 15°C to 24°C. The heat energy supplied was 2400 J. Calculate the specific heat capacity of water.

## Slide 78: Measure the Specific Heat Capacity of water by an Electrical Method
Using voltmeter and ammeter
Calorimeter
Lagging
Thermometer
Insulated Lid
Water
Heating Coil
V
A
Timer
Mass Scales
DC power

## Slide 79: Method
Record the mass of the calorimeter with and without water. Use cool water about 5 K below room temperature. Record temperature.
Switch on the power and the timer.
Ensure constant current.
Stir or agitate.
Record I and V once a minute.
When the temperature reaches about 5 K above room temp, stop and note the time and temperature.
V
A
Timer
Timer

## Slide 80: Measurements
Mass of copper calorimeter
Mass of cold water
Start temperature
End temperature
Current
Voltage
Time

## Slide 81: Calculation
Electrical Energy = Heat gained by copper and water
Re-arrange

## Slide 82: Sample results
Results:
Mass of calorimeter | 65 g
Mass of calorimeter + Water | 158 g
Start temperature | 17.4
Final Temperature | 23.5
Time taken | 6 mins
Current | 1.2 A
Voltage | 5.7 V
4068

## Slide 83: Using a paper cup instead of a copper calorimeter
Paper cup
Copper Calorimeter
The paper cup version results in simpler calculations because the cup has a very low heat capacity C and thus you can ignore the heat that goes into the cup.
This simplification introduces a systematic error, but it is of a similar magnitude to errors caused by the calorimeter heat behaviour.
Notes: The assumption with the calorimeter is that it all reaches the temperature of the water. The top portion will not fully reach the water temperature and so the term will have an error. In addition, the top portion will radiate more heat than the top portion of the paper cup version because it will reach a higher temperature than the un-imersed paper. In the past expanded polystyrene cups were used but these have been banned because they cannot be recycled, they produce microplastics and animals mistake them for food.
The paper cup calculations are easier to understand and may be a better place to start.
The assumption with the calorimeter is that it all reaches the temperature of the water. The top portion will not fully reach the water temperature and so the term 𝑚_𝑐 𝑐_𝑐 Δ𝜃 will have an error. In addition, the top portion will radiate more heat than the top portion of the paper cup version because it will reach a higher temperature than the un-imersed paper. In the past expanded polystyrene cups were used but these have been banned because they cannot be recycled, they produce microplastics and animals mistake them for food.
The paper cup calculations are easier to understand and may be a better place to start.

## Slide 84: Paper Cup Version
Simplified Calculation
Electrical Energy supplied= Heat gained by water
Re-arrange
Paper cup
Assumption: The heat transferred to the paper cup is negligible.

## Slide 85: Measure the Specific Heat Capacity of copper
Paper cup
Lagging
Water
Heat
Mass balance
Digital thermometer
Copper pellets
Boiling water

## Slide 86: Method
Measure the mass of about 30 g of copper pellets and transfer to a boiling tube
Heat pellets to 100°C in the tube immersed in boiling water (heat for about 5 minutes to ensure the pellets have reached 100°C).
Pour cold tap water (about 30 g) into a small insulated paper cup. Record its mass.
Insert a digital thermometer into the water and note the temperature.
Pour the hot copper pellets into the water, stir and record the maximum temperature.
Paper cup

## Slide 87: Results and calculations (paper cup)
 | Sample results | 
Mass of copper | 32 g | 
Mass of Water | 35 g | 
Start temperature | 17.4°C | 
Final Temperature | 23.5°C | 
Heat in = Heat out
Result:
365 J kg⁻¹ K⁻¹

## Slide 88: Latent heat (hidden heat)
CC0
Notes: Water at boiling point thrown into very cold air. The hot water has very low surface tension thus it splits into tiny droplets so small that they freeze on contact with the cold air. This demonstrates two things:
the lowering of surface tension due to heating is a manifestation of the greater potential energy of the molecules (bonds between molecules are weaker)
2. The increased surface area (thousands of tiny droplets) allowing for faster heat transfer so it has time to freeze while still in the air. This is not on the course, but it’s interesting and you can find a few nice videos on YouTube.

## Slide 89: The States of Matter
Liquid
Solid
Gas
Melting
Solidifying or freezing
Evaporating or vaporising
Condensing
Heat energy added
Heat energy removed
We do not study the plasma state.

## Slide 90: Draw a graph of Temperature vs added energy as a substance changes state.
Temperature (°C)
Energy supplied (J)
Latent heat of fusion
Latent heat of vaporisation
Boiling point
Melting point
Temperature remains constant for a period

## Slide 91: Particle model of states of matter
Solid: intermolecular forces hold molecules in a ridged structure. Particles vibrate. Liquid: Heat energy partially overcomes intermolecular force. Particles are still bound but can move around.
Gas: energy fully overcomes intermolecular force and molecules spread out.
Heat increases the energy of molecules

## Slide 92: Particle model for melting
Particles gain enough energy to move away from their equilibrium positions in the structure.
This allows them to move about freely.
Heat during melting increases their potential energy, not their kinetic energy.
Thus, the temperature of the material does not rise during melting.
Heat weakens the bonds

## Slide 93: Particle model for evaporation
At any given temperature there is a distribution of velocities among the molecules of any object.
Even below the boiling point, some molecules have sufficient kinetic energy in the right direction to break free from the surface.
When these leave, the average kinetic energy of the remaining particles is lower, and this is observed as a lowering of the temperature.
Heat breaks some bonds

## Slide 94: Particle model for boiling
Molecules gain enough energy to break the bonds with their neighbours.
Once again, this is a change in potential energy rather than kinetic energy
The temperature remains constant during the boiling process.
Heat breaks the bonds

## Slide 95: What is Latent Heat?
SI Unit = the joule (J).
The energy required to change the state of of an object with no change in temperature.
Based on HL 2014, 2025

## Slide 96: What is Specific Latent Heat?
The energy required to change the state of 1 kg of a substance with no change in temperature.
HL 2014, 2024
The SI Unit = joule per kilogram (J ​kg​-1​).

## Slide 97: What is Specific Latent Heat of Fusion?
Or … the amount of energy given off when it freezes.
CC0
The energy required to melt 1 kg of a substance with no change in temperature.
Based on HL 2014, 2025
Note the process occurs at the melting point temperature

## Slide 98: What is Specific Latent Heat of Vaporisation?
Or … the amount of energy given off when it condenses
CC0
The heat needed to evaporate 1 kg of a substance with no change in temperature.
Based on HL 2014, 2025

## Slide 99: Write the equation for Specific Latent Heat.
= Heat to change the state
= Mass
= Specific Latent Heat

## Slide 100: Summary C c L and l
 | An object | A substance
Change Temperature | Heat Capacity C Q=CΔθ | Specific Heat Capacity c Q=mcΔθ
Change state | Latent Heat L Q=L | Specific Latent Heat l Q=ml

## Slide 101: Example 12
Heat water to
It takes a huge amount of energy to convert water to steam. Calculate how much energy it takes to bring 30 g of water at 20°C to 100°C and then how much energy it takes to convert to steam.
Boil the water
= 10 032 J
= 69 000 J
Latent heat of vaporisation of water (l) = 2.3x106 J kg-1

## Slide 102: Example 13
20 g of ice at -18°C are added to 250 g of water at 26°C. Calculate the final temperature of the water and melted ice.
= Heat Lost (250 g Water) =
Heat gained (20 g Ice):
Specific heat capacity of ice: 2100 J Kg⁻¹ K⁻¹
Specific heat capacity of Water: 4200 J Kg⁻¹ K⁻¹
Latent Heat of Fusion Ice: 3.3 × 10⁵ J Kg⁻¹
Let = final temperature
Heat the ice
Melt the ice
Heat melted ice
27300-1050T
756+6600+84T =
(18) = 756
= 6600
84T
20 g of ice at -18℃
250 g of water 26℃
Note the 3

## Slide 103: Exercise
Q = ml = 0.032x3.34x105 = 1.069x104. J
How much heat energy is needed to melt 32 g of ice at 0°Cwithout raising its temperature?
Latent heat of fusion of ice: l = 3.34x105 J kg-1

## Slide 104: Exercise
40 g of ice at -18°C are added to 300 g of water at 25°C. Calculate the final temperature of the water and melted ice.
= Heat Lost (250 g Water) =
Heat gained (40 g Ice):
Let = final temperature
Heat the ice
Melt the ice
Heat melted ice
31500-1260T
14712+168T =
(18) = 1512
= 13200
168T
40 g of ice at -18℃
300 g of water 26℃
Note the 3
Specific heat capacity of ice: 2100 J Kg⁻¹ K⁻¹
Specific heat capacity of Water: 4200 J Kg⁻¹ K⁻¹
Latent Heat of Fusion Ice: 3.3 × 10⁵ J Kg⁻¹

## Slide 105: Verify mathematical models of heat energy, latent heat and temperature change using secondary data

## Slide 106: Exercise
Which model does the below graph verify, state how it verifies the model and calculate the heat capacity of the object.
Temperature (°C)
Heat kJ
30
1
20
40
2
The graph is a straight line which verifies the formula
Slope=20/1800. C=1800/20 = 90 J K-1
x
x

## Slide 107: Exercise
What step to ensure fairness has the student likely omitted. What is your best estimate of the heat capacity?
Temperature (°C)
Heat kJ
30
1
20
40
2
Adequate insulation / allowing too high a temperature
Best estimate is close to room temperature where heat loss is least significant
Steepest slope:
x
x

## Slide 108: Practical examples of Latent Heat

## Slide 109: Perspiration
Perspiration evaporates on your skin and takes the Latent Heat of vaporisation from your body. This brings your temperature down.
The specific latent heat of vaporisation of water is very high – hence this is a very effective process.
CC0

## Slide 110: Ice Pack
An Ice pack will keep things cold much longer than the same amount of a cold liquid.
It is the latent heat required to melt the frozen liquid that accounts for this difference.
CC0

## Slide 111: Heat Pumps and Fridges
Normally heat flows from hot to cold
A heat pump artificially reverses the direction.
Heat pumped from cold to warm region
A refrigerator uses a heat pump to remove heat from the interior

## Slide 112: Heat Pumps for home heating
Heat pumped from cold exterior to provide home heating
Consumes about one third the electricity of an electric resistance heater.

## Slide 113: Describe a Heat Pump
refrigerator on the left and a heater on the right
Low pressure liquid evaporates and takes in latent heat.
High pressure gas condenses and gives out latent heat
Cold side
Hot side
Compressor
Expansion Valve
Liquid
Liquid
vapour
vapour
Heat out
Heat in

## Slide 114: Demonstrate the effects of low pressure on boiling point
Water at 40°C
End blocked by finger or Blu Tack
Low pressure
Pull
blocked
syringe
Observation:
Water boils and cools
Notes: Not a mandatory demo. Helps appreciate the heat pump. It would be even better if you could monitor the water temperature.

## Slide 115: What are the properties of the refrigerant in a heat pump?
The refrigerant is the fluid that flows in the pipes.
low boiling point e.g. in a freezer it must be able to boil at a temperature of less than -18° C (at a low pressure).
high specific latent heat of vaporisation This makes the heat pump more effective.
1.
2.
Freon boils at -26 ° C

## Slide 116: HL 2016
In a heat pump, a fluid is used to transfer energy from a cold body to a warmer body.
Describe the operation of a heat pump and explain how a heat pump can be used to reduce the temperature of a cold region, for example the interior of a refrigerator. (12)
pipe containing a fluid (3) fluid changes state on passing through a valve/compressor (3) latent heat associated with fluid changing from liquid to gas (3) loss of temperature/heat in surroundings associated with fluid changing from liquid to gas (3)

## Slide 117: HL 2016
State two desirable physical properties of the fluid used in a heat pump.
high (specific) latent heat of vaporisation (3)
low boiling point / volatile / low molecular mass / little intermolecular forces (3)

## Slide 118: HL 2021
(v) Draw a labelled diagram of a heat pump.
compressor indicated (3)
(expansion) valve indicated (3)
correct arrangement of liquid/vapour indicated (3)
(vi) Explain how a heat pump works.
heat taken in by liquid evaporating (3)
heat given out by vapour condensing (3)

## Slide 119: Exercise
A student placed 4 kg of water at 12°C in a small fridge. The fridge had an electrical energy consumption meter attached. After 20 minutes the water is removed and these readings are taken: Electrical energy consumed: 60 kJ, Final temperature of water: 6°C. Calculate the coefficient of performance (COP) of the fridge where .
Heat transferred from water =
Note the COP of a heat pump is not a fixed figure, it depends on the temperatures on both sides of the heat pump
E

## Slide 120: Measure the Latent Heat and Specific Latent Heat of Fusion of Ice
Calorimeter
Insulated lid
Stirrer
Thermometer
Insulation
Cloth to dry the ice
Water
Mass balance
Crushed ice

## Slide 121: Method and results
Mass of calorimeter ________
Add warm water (~35° C, half full),
Combined mass ________
Place in insulation
Crush ice,
When it starts to melt, dry it
Take temperature of the warm water ______
Add ice to increase the volume in the calorimeter by about 20%
Stir until ice melted
Take final temperature _______
Take final mass _______
_____
______
Subtractions:

## Slide 122: Calculation of L (OL&HL) and l (HL):
Heat lost = heat gained
Heat lost by water | + | Heat lost by calorimeter | = | Latent heat gained by ice | + | Heat to bring melted ice to final temp
Heat lost by water | + | Heat lost by calorimeter | = | Latent heat gained by ice | + | 
Water
ice
Heat
Practice the method, don’t try to learn the equation because it can change.

## Slide 123: Exercise on Sample Results
Mass of calorimeter ____________
Combined mass ____________
temperature of water __________
final temperature _______
Final mass _______
Calculate and for the ice using this data:
_____
______
Subtractions:
62.1 g
97.3 g
31.7°C
9.7°C
106.5 g
=2919 J
= 385
=

## Slide 124: HL 2019 2024
Why did the student crush the ice?
To ensure that it would have an even temperature – ie temperature in the middle of a particle of ice = temperature on the surface.
To expose more surface area so that it will all melt more quickly.
Why did the student dry the ice?
To ensure that when he calculated the mass of the ice (by subtraction) that he got an accurate figure. If there was water mixed in, then he would not get the true mass of ice.

## Slide 125: HL 2017
How did the student prevent heat loss?
Insulated the container
Used an insulated lid
Give two characteristics of the thermometer (2017, 2024)
Measures in steps of 0.1 ℃
Low specific heat
Fast reacting

## Slide 126: Specific latent heat of vaporisation
Calorimeter
Insulated lid
Thermometer
Insulation
Water
Mass balance
Dry Steam
Secondary Data
Measure:
Mass of calorimeter
Mass of water before and after steam
Temperature before and after steam
Notes: The vaporisation experiment is only partially described here and is not recommended. The latent heat of fusion (ice) experiment is more fully described. It is much safer and on its own meets the requirements for collecting primary data for latent heat. Students are only required to collect primary data for one type of latent heat experiment. Risks associated with the vaporisation experiment include stoppers ejected at speed from flasks under the pressure of the steam, connections breaking under pressure and hot steam ejected in an unexpected direction, burn and fire risk from bunsen or hot plate. Precautions can be taken but they can also be forgotten.

## Slide 127: Key points
Start with water cooler than room temperature (e.g. add ice)
Dry the steam (steam trap)
Don’t over-heat the water (30 seconds for small calorimeter)
Write a conservation of energy equation.

## Slide 128: Write an equation
Heat lost = heat gained
By what?
Heat lost by steam = heat gained by water and copper
Be more specific.
Latent heat lost by steam
Heat lost by condensed steam as it drops to the final temperature
Heat gained by water
Heat gained by copper
=
+
+
Start with conservation of energy

## Slide 129: Equation continued
Learning this equation is a bad strategy you can be asked a variation.

## Slide 130: Exercise (steam)
Calculate the latent heat and the specific latent heat of the steam (HL 2010)
Mass of calorimeter: 34.6 g
Mass of calorimeter + water: 96.4 g
Mass of calorimeter + water + steam: 97.6 g
Temperature before adding steam: 8.2
Temperature after adding steam: 20.0
L=

## Slide 131: How and Why did the student dry the steam?
Use a steam trap
How?
Why?
If there was water mixed with the steam, it would add to the final mass but would not contribute any latent heat.
Steam traps collect droplets of condensed steam

## Slide 132: How and why did the student cool the water?
Cool in fridge / melt some ice in it
How?
Why?
Minimise heat loss errors… Heat gained from surroundings at start heat lost to surroundings at end.
lower temperature gradients = lower heat loss

## Slide 133: If there was un-melted ice in the calorimeter when you introduced the steam how would it affect the result?
Some of the added heat would be used in melting the ice (latent heat of fusion). This heat would not contribute to a rise in temperature. Thus, the final temperature would be too low.

## Slide 134: Heat Transfer
Convection
Conduction
Radiation

## Slide 135: What is Convection?
Heat transfer by means of circulation of a fluid. HL 2018, 2024
Heat
Remember a fluid is a liquid or a gas

## Slide 136: Demonstrate Convection in a Liquid
Heat
Carefully add a drop of food colouring to the bottom of a beaker of cold water with a plastic pipette.
Heat.
Observation
The water and coloured dye circulates showing convection currents.
Food colouring

## Slide 137: Explain Why Convection Occurs
Heated liquid expands and becomes less dense.
It rises to float on denser cool liquid.
Thus, the cooler liquid sinks and gets heated.
This movement is called a Convection Current.
Heat

## Slide 138: Particle model simulation: Convection
Convection - Javalab
Link :
Objective: observe the general flow of the gas
Observe the back-and-forth motion of the particles

## Slide 139: What is meant by Conduction of heat?
Conduction is transfer of heat by vibration from particle to particle with no net movement of the medium. HL 2018, 2024

## Slide 140: Particle model simulation: Conduction of heat
Particle Simulation of Thermal Conduction - Javalab
Link:
Objective:
Observe how vibrations propagate from particle to particle.
Observe how heat flows without any net movement of the substance.

## Slide 141: Demonstrate how different solids conduct heat at different rates
Use rods of the same size.
Stick identical weights on the end of each rod with wax.
Pour in hot water.
Observation Weights fall off Aluminium first then steel then wood.
Steel
Hot water
Weights stuck on with wax
Aluminium
wood
Conclusion: aluminium is the best conductor of heat

## Slide 142: Demonstrate that water is a poor conductor of heat
Ice
weight
Observation
Ice takes a long time to melt.
Apparatus see diagram.
Method Heat top of water
Conclusion Water is a poor conductor of heat.

## Slide 143: What is Radiation of Heat?
Radiation is the transfer of heat energy by means of electromagnetic waves. It will pass through a vacuum. HL 2018
CC0

## Slide 144: What is the Solar Constant?
The amount of solar energy falling normally on the earth per second per square meter. HL 2023
Watts
per square metre
Its value is about 1.36 kW ​m​-2​.
also called the Solar Irradiance.
1 m2

## Slide 145: Example 14
Energy = Solar constant x area x time
The solar constant is 1.36 kW m⁻². How much energy falls on a 0.9 m x 1.5 m solar panel in one minute? Round your answer to 4 significant figures.
Note, using 6 significant figures does not make sense here because the solar constant is only given with 3 significant figures

## Slide 146: Exercise
The solar constant is 1.36 kW m⁻². How much power can be obtained from 6 solar panels measuring 0.9 m by 1.3 m if the system efficiency is 21%?

## Slide 147: Demonstrate that dark colours radiate heat better
Observation:
The temperature of the water in the black can falls quicker.
Cans filled with hot water, one shiny the other painted matt black
Thermometers
Apparatus: see diagram
Method: fill cans with hot water and monitor the temperature
Notes: Not mentioned in the spec but part of transfer of heat and insulation

## Slide 148: Demonstrate that dark coloured objects absorb heat better than bright or shiny ones
Cold water & direct sunlight.
Observation the darker can will heat up at a faster rate.
Sunlight
Thermometers
Cans with cold water
video:
INFRA-RED RADIATION - Science GCSE Physics Required Practical

## Slide 149: What is meant by the U-Value of a material?
The SI Unit of U-value is W m-2 K-1
Heat
1 m2
The rate of energy transfer through 1 m2 of a surface when there is a temperature difference of 1 K across the surface. HL 2022D
What is the SI unit:
1 K colder

## Slide 150: Where is U-value in the formula book?
Page 58 under heat and temperature
What is ?
= heat conducted per second
(measured in watts)

## Slide 151: Use the formula to recall the definition of U-value
per second
per
per Kelvin
re-arrange:
Page 58
Heat energy
Energy per second per per K

## Slide 152: Which is the better insulator: high or low U-value?
U = Watts per square meter per K
High U-Value = More watts = Bad Insulator
Low U-Value = Less watts = Good Insulator
Heat
1 m2
W m-2 K-1

## Slide 153: Leaving Cert 2014
Rate
Heat loss
The U-value of the material in a double-glazed window is 2.8 W m⁻² K⁻¹. The window has an area of 3.0 m². How much energy is lost through the window in one hour if the temperature inside is 20℃ and the outside temperature is 11℃?
Page 58

## Slide 154: Leaving Cert 2022 deferred
marking scheme:

## Slide 155: Example 15 Impact of insulation
A home-owner is considering replacing windows. Old U value 3.2 W m⁻² K⁻¹ New U-value 1.2 W m⁻² K⁻¹ Total window area 20 m². Calculate the reduction in power consumption in watts when the indoor temperature is 20℃ and the outside temperature is 7℃.
Old windows:
New windows:
20(3.2)(13)
=832 Watts
20(1.2)(13)
=312 Watts
Saving: 832-312=520 W

## Slide 156: Exercise
Calculate the difference in heat loss between an old window measuring 2 m x 1.5 m with a U-value 5 W m⁻² K⁻¹ and a new window of the same size with a U-value of 1.3 W m⁻² K⁻¹ when the temperature difference between inside and outside is 15℃
Old window:
2(1.5)(5)(15)
=225 Watts
New window:
2(1.5)(1.3)(15)
=58.5 Watts
Difference: 225-58.5 = 166.5 W

## Slide 157: Exercise (part 1)
A student filled a cup with hot water and measured the temperature of the water every 4 minutes. Plot a graph temperature difference (Δθ) between the inside and outside of the cup vs time. Room temperature = 20 ℃
Time (mins): 0 4 8 12 16 20
Temperature (℃): 80.2 70.9 63.7 58.0 53.8 49.8
(K)
60.2 50.9 43.7 38.0 33.8 29.8
(K)
Time (min)
20
10
0
0
20
40
60

## Slide 158: Exercise (part 2)
The student expanded the centre part of the graph. Use this to determine the temperature drop per second when the temperature difference is 40℃.
Slope at 40℃:
Use two equidistant points:
Slope
Temperature drop per second
X
Time (min)
(K)
12
10
8
35
40
45
9
11
X
Notes: See SEC sample paper 2 Q7 where the student was asked to find the slope of a magnified portion of a non-linear graph. The magnified portion was approximately linear similar to his portion of the graph.

## Slide 159: Exercise (part 3)
If the mass of water was 100 g, determine the heat loss in joules per second when the temperature difference is 40℃.
T

## Slide 160: Exercise (part 4)
If the surface area of the cup in contact with the water was 95 cm², calculate a U-value for the plastic of the cup using the value you calculated for heat loss per second in the previous question. The formula for U-value is
= 24 W m⁻² K⁻¹
Note: At higher temperatures, a lot of heat is lost due to evaporation rather than through the sides of the cup. This creates a systematic error.

## Slide 161: Impact of insulation on efficiency and sustainability
i.e. heat loss is proportional to
Surface area, U-value, Temperature difference
So, we should live in spherical dwellings built from thick insulating material and keep the indoor temperature as low as bearable.
CC0
Research question: write a piece on the pros and cons of igloos. Reference your sources.

## Slide 162: Example 16
Describe the mechanisms by which heat escapes from this container.
Heat source
Air
Heat is circulated inside by convection.
And heat is radiated towards the walls by radiation.
Inside surface gets hot.
Heat is transferred through the walls by conduction making the outside surface hotter than the surroundings.
Heat leaves the outside walls by convection and radiation.

## Slide 163: Efficiency

## Slide 164: How is percentage efficiency calculated?
Percentage efficiency
Note Efficiency is also covered in Section 1.4

## Slide 165: Can you use energy instead of power?
Percentage efficiency
Yes

## Slide 166: Give examples of Improving efficiency
Heat pumps that consume less power for a given output
Lights and motors that consume less power for a given useful output
Energy storage devices (e.g. batteries) that consume less power for a given output
A kettle that uses less power to heat the same mount of water.

## Slide 167: Exercise
A 2-kW kettle takes 6 minutes to bring 1.8 kg of water from 18°C to 100°C, calculate the efficiency.
Specific heat capacity of water = 4184 J kg⁻¹ K⁻¹
= 86%

## Slide 168: Revision summary
Key definitions: Heat, Temperature, Absolute zero, kelvin, Thermometric properties, Thermocouple, Thermistor, Heat Capacity, Specific Heat Capacity, Latent Heat, Specific Latent Heat, Efficiency, U-value, conduction, convection, radiation.
Solve problems using ,
Describe and explain heat pump, melting, evaporating, solid, liquid, gas, conduction, convection, radiation using particle model and mathematical models where appropriate.
Experimental: Compare thermometer materials (primary and secondary data). Determine and using primary and secondary data. Verify heat models with secondary data.
Investigate insulation vs energy consumption using secondary sources.